| PROPOSAL TRANSMITTAL FORM for DESIGN-BUILD PROJECTS (DB-PTF) |  |  |
| --- | --- | --- |
| Project Number: | 630-036-008 |  | Date RFP posted | February 5, 2018 |
| Project Description | Construct Salt Storage Building |  |  |  |
| Project Location | New Lenox, Will County |  |  |  |
| Project Manager | Abdulgaffar Shedbalker |  | Date due | March 7, 2018 2:00PM |
|  | Suite 14-600 100 W. Randolph St. |  |  |  |
|  | Chicago, IL 60601 |  | Submit Proposal | Suite 14-600 |
| Phone Number |  |  | To: | 100 W. Randolph St. |
| Fax Number | 312-814-4443 |  |  | Chicago, IL 60601 |
| e-mail | 312-814-2041 |  |  |  |
| Brief Description of Project: |  |  |  |
| Elements of the project will include construction of a permanent pre-engineered salt storage building capable of storing 10,000 tons of salt. The scope also provides for siting, lighting, ventilation and concrete structural walls, foundation and footings. ALTERNATE BID NO. G-1 (AB-G1): Extend the base bid building design an additional fifteen feet, (15’ – 0”) to an overall length of +/- 215’-0” (varies by fabric roof manufacturer). The north wall location remains same as base building. The interior HOLD dimension becomes 212’-0”. Extension is to the south. Include all required structural and electrical components. No additional interior, (F1) lighting is required. Lighting Plan as indicated herein shall remain as indicated. One additional block heater outlet on West elevation shall be added @ 15’- 0” o.c.. Adjust size of Exhaust Fan, intake and exhaust louvers as necessary for the increased interior volume of the building as appropriate per code. Make all adjustments to final grading design as indicated on plans for AB-G1. ALTERNATE BID NO. G-2 (AB-G2): Extend the base bid building design an additional thirty feet, (30’ – 0”) to an overall length of +/- 230’-0” (varies by fabric roof manufacturer). The north wall location remains same as base building. The interior HOLD dimension becomes 227’-0”. Extension is to the south. Include all required structural and electrical components. Base building design interior lighting, (F1 fixture) layout is adjusted as follows: Shift the base building layout 30’ south and insert one additional row, (2 additional F1 fixtures) 30’ north of the northern most, (last) row. Two additional block heater outlets on West elevation shall be added at 15’- 0” o.c.. One additional F2 wall pack fixture shall be added to the west elevation by changing the spacing to three equal spaces between the fixtures and moving the end fixtures to 25’ inset from each end wall. Adjust size of Exhaust Fan, intake and exhaust louvers as necessary for the increased interior volume of the building as appropriate per code. Make all adjustments to final grading design as indicated on plans for AB-G2. |
| Project Budget (Design and Construction) | $ | 1,685,700.00 |
| Project Time (Design and Construction) from ATP | 180 | Days |
| Attachments: |  |  |  |  |

| DB-PTF | Part 2 To be completed by Offeror |  |
| --- | --- | --- |
| Phase 1 Requirements |  | Date submitted |  |
| Firm Name |  |  | Contact person | (name) |
| Address | (Address) |  |  | (phone) |
|  | (Address) |  |  | (fax) |
|  | (Address) |  |  | (e-mail) |
|  | (Address) |  |  |
|  |  |  | Phase 1 submittal | ( |
| TIN number |  |  | Phase 2 submittal | ( |
| Acknowlegment of Amendments (Phase 1 and Phase 2) |
| Amendment No. |  |  |  |  |  |  |  |  |  |
| Date |  |  |  |  |  |  |  |  |  |
| Phase 2 Requirements |
| List the firms providing the following work (per 00 42 10.3B.). Updated disclosure Form C must be provided by each firm listed. |
|  | Firm name/CDB firm no. |  | TIN |
| Architect |  |  |  |
| Engineer |  |  |  |
| General |  |  |  |
| Plumbing |  |  |  |
| Heating |  |  |  |
| Ventilating |  |  |  |
| Electrical |  |  |  |
| Statement of Compliance |
| *Offeror hereby certifies that all items submitted in this proposal and final design documents (after contract award) comply with the RFP requirements. The criteria specified in the RFP for Project No. 630-036-008 are binding contract criteria and in case of any conflict after award between the RFP and the contractor's proposal, the Request for Proposal criteria shall govern unless there is a written and signed agreement between the contractor and the CDB waiving a specific requirement. Should this proposal result in the award of a contract this statement will be included on each sheet of the drawings and on the cover of the specifications. |
| Name of Person Authorized to Sign Proposal | Signature | Date |
| Exceptions attached: | Yes |  | No |  |  |  |  |